OPTICAL FIBRE IN COMMUNICATION
Shubha Gokhale
School of Sciences, IGNOU

---
Optical Fibres in Communication

---
Advantages of OF Communication
High information capacity of fibre: digital communication bit-rates of up to 14 Tbit s-1 have been reached over a single 160 km line
Low attenuation and dispersion: <0.3 dB km1
Space saving: due to extreme thin dimensions (total diameter < 500 μm) of fibre the coefficient of information capacity to cable cross section is high
Low cross-talk: does not generate any interference to other systems

---
Advantages of OF Communication (Contd…)
Immunity to EMI: free from EMI pick ups, including lightening, sparking etc.
Higher security: no radiation of EM waves involved hence tapping difficult
Low cost: relative to the metallic coaxial cables and due to wide spacing between the repeaters.
Abundance of basic resource: Silica
Easy maintainability

---
Limitations of OF Systems
Optical fibre needs special technique of splicing to connect to other fibre.
Due to small dimensions the fibre coupling needs great accuracy in alignment (of few m)
Every time the signal needs amplification, it needs to be first converted to electrical signal, then amplified using electronic amplifiers and then again converted back into optical signal

---
Working Principle of OF

---
Critical Angle
Snell’s Law
n1 sin 1 = n2 sin 2
where 1 is angle of incidence and 2 is angle of refraction
At critical angle, C , 2 = 90 sin 2=1

---
Construction of Optical Fibre
Core refractive index (n1) > cladding refractive index (n2)
Typical diameter of core ~ 5-10 μm
Cladding diameter ~10-15 times core diameter

---
Acceptance Angle
a is the maximum angle to the axis at which light may get propagated in the fibre and is called the acceptance angle.

---
Numerical Aperture
n0 sin 1 = n1 sin 2 = n1 cos 
for 1 = a	= C
n0 sin θa is known as Numerical Aperture

---
Example
A silica optical fibre with a core diameter of 30 m has core refractive index of 1.50 and a cladding refractive index of 1.47. Its input end is immersed in water. Calculate :
the critical angle at the core-cladding interface
the NA for the fibre
the acceptance angle for the fibre in water
(Refractive index of water is 1.33)

---
Critical Angle Determination
The critical angle c at the core-cladding interface is given by

---
Numerical Aperture Calculation
The numerical aperture is given by:

---
Acceptance Angle in Water
Acceptance angle in water can be obtained by using :

---
Modes of Optical Transmission
Geometric optics approach does not hold good for small diameters
The ray theory model describes only the direction of a plane wave component in the fibre It does not take into account interference between such components.
Due to interference phenomena only rays with certain discrete characteristics propagate in the fibre core.
Fibre supports only limited number of discrete guided modes.

---
Modes in Optical Fibres
A mode is a stable propagation state in an optical fibre.
The number of modes that can be propagated in a fibre depends on
Refractive index of core and cladding
core diameter
wavelength of the propagating light
The core diameter can be reduced to achieve single mode of operation.

---
Classification of Optical Fibres
Based on the number of modes propagating in a fibre:
Single-mode (SM) fibre
Multi-mode (MM) fibre
Based on the gradient of refractive index value of core :
Step index (SI) fibre
Graded index (GI) fibre

---
Step Index Fibres
SI SM
SI MM

---
Graded Index Fibre
GI MM

---
Signal Attenuation in Fibre
Signal gets attenuated while getting transmitted through the fibre
L = 10 log10 (Pout / Pin)
Depending upon the attenuation, spacing between the repeaters is decided

---
Intrinsic Losses in Fibre
Losses occurring due to fibre material and structure imperfection
Rayleigh scattering due to structure imperfection
Absorption by (impurity) ions in the fibre
Geometric parameter variation
Microbending

---
Extrinsic Losses in the Fibre
Losses occurring due to external factors
Fibre connection losses
  - Splicing losses
  - Connector losses
Fibre bending losses

---
Telecommunication Windows
Preferred wavelengths of operation:
850 nm
1310 nm
1550 nm

---
Chromatic dispersion
Also known as Material Dispersion
Caused by variation of refractive index with wavelength of the light passing through the material
Different wavelength (colour) light travel with different speeds and emerge out at different times
Usually does not affect normal operation as single wavelengths are used in communication

---
Modal Dispersion
GI MM fibre can take care of modal dispersion to some extent
Different Modes

---
Modal Dispersion and Data Handling
Optical fibre is mostly used for handling digital (binary) signals in form of pulses
Number of bits transmitted per second determine the capacity of data handling
If modal dispersion widens the pulse, the spacing between two pulses needs to be increased in order to avoid inter-mixing of consecutive pulses. This reduces the capacity
Advisable to reduce the modal dispersion

---
Optical Communication System
Apart from fibres, optical communication system comprises of opto-electronic converters :
Electrical – optical converter has optical source driven by electrical signal
Optical – electrical converter has optical detector that senses signal emerging out of fibre and produces corresponding electrical pulses

---
Optical Sources
Incandescent light
LED
Laser Diodes
  - Sources should be small, focused for better fibre coupling
  - Incandescent lights not preferred due to its white nature

---
Optical Sources :LED
Light Emitting Diode is a semiconductor diode with direct band gap materials
Monochromatic, small size, easy fabrication
  - GaAs: IR
  - AlGaAs: Red
  - GaAsP, GaP: Orange, Yellow
  - InGaN/GaN: Green
  - ZnSe: Blue
  - ZnSe/ Phosphor: White

---
Optical Sources : Laser Diode
Laser diodes are degeneratively doped semiconductor p-n junctions made of direct band gap materials
Highly monochromatic, coherent, small divergence, high intensity
  - InGaN : Blue-violet
  - AlGaAs: Green
  - AlGaInP: Red, IR

---
Characteristics of Optical Sources

---
Optical Detectors : Photodiode
Reverse biased semiconductor junction diode with depletion and diffusion regions.
Diffusion is slow process hence detection bandwidth is low.

---
Optical Detector : p-i-n Diode
This geometry allows absorption of photon in larger area (intrinsic layer that acts as wider depletion region)

---
Applications of Optical Fibres
Communication
Sensors
Illumination
  - Light guides in medical field
  - Imaging optics in endoscopy
  - Sunlight guide for buildings
  - Decorations
  - Imaging optics in endoscopy
  - Light conduction in spectrometers

---
Thank You!