        AIM:-TO DETERMINE THE SOLUBILITY OF DIFFERENT SALTS i.e. LEAD SULFATE & BARIUM SULFATE

---
REQUIREMENTS:-Conductivity meter, two beakers of 100 ml, glass rod, wire gauze, lead sulfate salt, barium sulfate salt &water.

---
THEORY:-
- Conductance:-
- it is the ability of a material to pass electrons. It is the opposite of resistance. Metallic conductance takes place through the flow of electrons current in the solution is carried by ions. Only those substance will conduct electricity that are ionic in molten state or dissociate to form ions when dissolved in the solvent. The solution that conduct electricity are known as electrolyte.
- To measure the conductance of an electrolyte solution , it is placed in cell having two electrodes that are connected to an external battery. Such a cell is known as electrolytic cell.
- The conductance of a solution is equal to sum of the conductance of each individual electrolyte as well as conductance of water. G=G1+G2+G3--------------Gwater.
- Electrolyte solution obeys ohms law, G=k (a\l), where , l =length of the electrode, a=area b\ w the two electrodes, k= specific conductance.

---
PROCEDURE:-
- About 8g of the finely powdered lead sulfate was taken.
- That was shaken repeatedly with approximately 50 ml of hot water so that any soluble impurities present were completely removed.
- This , well washed salt was placed with 400 ml of water in a beaker.
- The contents were shaken time to time.
- Finally the conductance of clear lead sulfate solution was determined by taking a quantity of solution from a beaker to the conductivity cell.
- The same procedure was repeated for barium sulfate salt.

---
Observations and calculations:-
- For lead sulfate salt :-
- S=1000xk\^ K=G X CELL CONSTANT K=0.99 X 1 =0.99 ^=4.72 S=1000 X 0.99\4.72 S=209 g /l
- For barium sulfate salt:- similarly ,S= 1000 x0.99\1.72 S=575 g /l

---
RESULT:-
The solubility of lead sulfate salt was found to be 205 g /l
The solubility of barium sulfate salt was found to be 575 g /l
        PRECAUTIONS:-
1.The clear solution should be used.
2.There should be properly insulated to avoid stray leakages of current.